## Slide 1: Look, Ma, No BIOS!
A Hands-Off Introduction To LinuxBIOS
Oleg Goldshmidt
IBM Haifa Research Laboratory

## Slide 2: BIOS Milestones
Early 1970ies: Gary Kildall’s 50 mile commute
  Intel’s 8080, Interp/80, PL/M
  Intel’s Intellec-8 (microprocessor + memory + terminal port – storage)
  IBM’s (8 inch, $500) floppy disk
  John Torode – floppy controller, Gary Kildall – CP/M (Control Program/Monitor)
1976: Intel loses interest, Imsai (and a 100 other companies) need an OS
  Kildall splits CP/M into hardware-independent part and hardware-specific BIOS
Around 1980: IBM in Boca Raton make the PC (Acorn) – in 1 year
  Broke every IBM rule by making an open system, published all specs
  Published – and copyrighted! - BIOS code
1981: Rod Canion, Jim Harris, and Bill Murto at Houston’s House of Pies
  Business plans on placemat: Mexican restaurant, build HDs, car key finder
  Winner: reverse engineer BIOS to make a 100% IBM-compatible PC
  Investment: 15 senior programmers, several months, $1MM
Around 1982: Phoenix sells IBM-compatible BIOS chips for $25

## Slide 3: How BIOS Works
From the cold state a special hardware circuit sends a signal to the RESET pin of the CPU
Some registers (cs, eip) are set to fixed values, and the code found at physical address 0xfffffff0 is executed
  The address is mapped by hardware to BIOS ROM chip
Linux does not use BIOS routines, BIOS must be executed in real mode
  Only real mode addresses (seg*16+off) are available in the cold state
  No GDT, LDT, or paging are needed, must be initialized in real mode
Major BIOS tasks
  POST
  Hardware initialization (e.g. PCI configuration)
  Search for an OS to boot (configurable)
  Copies the first sector of the boot device to RAM (at 0x00007c00), jumps to it, and executes
Invokes the bootloader

## Slide 4: How Bootloader Works
Floppy
  The instructions in the first sector are loaded into RAM and executed
  Bootloader copies itself from 0x00007c00 to 0x00090000
  Sets up real mode stack
  Invokes a BIOS procedure to load the setup() code to 0x00090200
  Invokes a BIOS procedure to load the rest of the image from 0x00100000
  Jumps to setup() code
Hard Disk
  The first sector (MBR) contains the partition table and a small program that loads the first sector of the partition with the chosen OS
  Some OS (e.g. Win98) identify the boot partition with an “active” flag
    Only the OS whose image is on the active partition may be loaded
  Sophisticated programs such as LILO or GRUB may allow runtime choice of image
  LILO’s first stage is loaded to 0x00007c00, moves itself to 0x0009a000, sets up real mode stack, loads second stage to 0x0009b000
  User chooses kernel, the rest is similar to floppy
  Execution jumps to setup()

## Slide 5: How setup() Works
The setup() function is loaded at offset 0x200 of the kernel image file
Initializes hardware devices and sets up the kernel execution environment
  But Linux sometimes relies on BIOS for initialization
Major operations
  Invokes a BIOS procedure to determine the amount of RAM
  Initializes keyboard
  Initializes the graphics adapter
  Reinitializes the disk controller
  Checks for buses, bus mice, APM, etc
  If needed, moves the kernel image to make space for decompression
  Sets up the Interrupt Descriptor Table (IDT) and a Global Descriptor Table (GDT)
  Remaps the interrupts (BIOS maps hardware interrupts to the CPU exception range)
  Switches to protected mode
  Jumps to startup_32(), which starts the kernel proper

## Slide 6: BIOS Today: A Pain In Sensitive Parts Of Anatomy
Clusters (started at Cluster Research Lab, Advanced Computing Lab, LANL)
  Nodes depend on vendor-supplied BIOS for booting
  BIOS normally relies on inherently unreliable legacy devices (floppy, HD) to boot the OS
  BIOS cannot deal with non-standard, experimental hardware Need full control of the boot process, to the point that jobs in the queue might indicate which kernel to run, where to find root FS, etc.
Maintenance is a nightmare
  BIOSes are buggy and cannot be fixed (by user)
  The development toolchain is highly specialized (read: obsolete), difficult to come by, can be quite expensive
  Try wandering around a few hundred node cluster with a monitor and a keyboard to change one BIOS setting
Get rid of the legacy BIOS altogether!

## Slide 7: Requirements and Decisions (As Specified by LANL)
Starting point: the current status of netboot on PCs
  netboot has been available on Suns for more than 15 years
  on PCs, BIOS and PROM must be in 16-bit mode - 8086 (6MHz, 25 years old CPU) emulation, all sorts of weird stuff such as near and far pointers, etc
  standards: NIC boot model has to conform to NDIS2 (16-bit Windows model), thanks to Microsoft and Intel
Requirements
  load something onto CPU that can load boot parameters over network, find out what to do, and load an OS kernel
  open source – nothing proprietary
  portable: no (or minimal) assembly, support a variety of NICs, motherboards
  avoid reinventing the wheel – try to use code that supports lots of hardware etc
  support standard protocols – NFS, bootp, etc
Write netboot from scratch or use a minimal Linux kernel?
  custom netboot will duplicate OS (Sun netboot – no support for AFS, msdos, etc)
  no real space savings (netboot – 128K, minimal Linux – 300K)

## Slide 8: Operation, Benefits and Disadvantages of LinuxBIOS
Gunzips Linux out of flash (NVRAM)
  No moving parts but the fan
  Minimal amount of hardware initialization, Linux does the rest
  Kernel boot times (not system start) as fast as 3 seconds
Using a real OS rather than simple netboot or BIOS is more flexible
  Linux can boot over Ethernet, Myrinet, Quadrics, SCI
  Cluster nodes can be as simple as CPU + memory + network
Boot diagnostic and maintenance over serial port
Not all motherboards are supported
Hardware manipulation may be involved

## Slide 9: LinuxBIOS Do-It-Yourself HOWTO
Check whether the motherboard is supported
  The BIOS chip must be removable from its socket
Hardware needed:
  Disk-on-Chip (DoC) memory device to be plugged in instead of the BIOS chip (8 MByte instead of 2 Mbit)
  32-pin ZIF (Zero Insertion Force) socket to make swapping chips easy and safe
  “development” and “target” machines (can be the same), BIOS chip in ZIF on target
Install Linux on target, including DoC support (as module)
Configure and build LinuxBIOS, a patched kernel (working, not latest), and MTD utilities (“erase”, “flash_on”). NB: source code changes may be needed.
With power on, remove the BIOS chip from ZIF and insert the DoC
Burn LinuxBIOS into DoC using the “burn_mtd” utility
Reboot (through power cycle) while saying the appropriate prayers to root (“Root, G-d, what is difference?”)

## Slide 10: Swapping The BIOS Chip
The ZIF socket plugged into the motherboard, with the original BIOS chip inserted (both images are from the Linux Magazine article on LinuxBIOS)
Inserting the DoC into the ZIF socket. WARNING: BE ADVISED THAT THIS STEP CAN HURT OR KILL YOU! If you haven't done this, or are not trained, or have a history of getting hurt by hardware, DON'T DO IT.

## Slide 11: What Can Go Wrong
any time you stick your hand into an open machine while the power is on, you're risking life and limb (ESD), and YOU CAN MESS UP THE HARDWARE:
incorrect insertion of the flash (shown)
  reverses power and ground
  the DoC gets very hot (see the molten sticker)
incorrect jumper settings
aggressive and/or inappropriate use of metal objects such as screwdrivers
miscellaneous miswirings and mishandlings

## Slide 12: After LinuxBIOS Boots: Troubleshooting etc.
If you see a penguin instead of the normal BIOS logo – your prayers have been heard…
No HD, keyboard, ethernet, root FS? Not to worry – can be sorted out. The main thing is to have the kernel running.
No penguin? You have not said the right prayers:
  Connect a null modem RS-232 cable to the first serial port on target
  Connect the cable to the development machine and start a 115200 baud, 8 bit, no parity serial terminal emulator
  Reboot and debug
Create a root FS on the DoC
  Enable a few more MTD options (to format, write the fs) in kernel, rebuild, and reboot
  Create a partition (~7MB) in the DoC, and format the fs
  Change the device that LinuxBIOS expects to find the root fs on
  What to put into the root fs? See Tom’s Root Boot or another tiny distribution.

## Slide 13: How It Works
32-bit mode from the start: load GDT and enable memory protection
  execute LGDT instruction and provide a pointer to a table descriptor
  no problem with having the table in NVRAM - takes about 10 instructions
Basic chipset initialization
  assembly code needed to turn DRAM on
  the rest can be done in C
Linux assumes hardware is initialized by BIOS. LinuxBIOS cannot assume this
  e.g. if IDE controller is not initialized then Linux assumes that BIOS disabled it
  one-line change to make the driver enable IDE by default
5 major components:
  protected mode setup
  DRAM setup
  transition to C
  mainboard fixup
  Kernel unzip and jump to kernel

## Slide 14: Protected Mode Setup: How To Run a Pentium
Puts segmentation, paging, TLB h/w in a sane state, turn on segmentation, not paging - 17 instructions:
  1st instruction, executed in 16-bit mode: jump to BIOS startup – a standard part of x86 reset
  5 instructions: disable interrupts, clear TLB, set code and data segments to known values
  1 instruction: load a pointer to GDT (to manage addressing in segmented mode)
  4 instructions: turn on memory protection
  6 instructions: do remaining segment register setup for protected mode
At this point we
  are running in protected mode
  can address 4GB of memory
  are running a Pentium, not a 8086

## Slide 15: DRAM, Transition to C, Mainboard Fixup, Starting Kernel
DRAM setup
  non-portable, tricky, tough to figure out
Transition to C
  set up the stack and call a function to do the rest
Mainboard fixup
  turn on cacheing (MTRR) so that the kernel unzips in reasonable time
    Otherwise it can take a minute or more
  make all the FLASH available (rather than 64K or 128K)
    requires some register manipulation, different for each chipset
  minimal power management capabilities
  do stuff Linux cannot (or will not) do:
    turn clock interrupts on
    a bit of PCI initialization – set Base Address Registers
Inflate and run the kernel (snarfed from the kernel itself)
  handle parameters, command line
  make gunzip work in ROM environment (declare initialized arrays const)
  jump to startup_32(), not to setup() as LILO does

## Slide 16: OK, How Do We Boot a Real Kernel from LinuxBIOS? LOBOS
LOBOS (Linux OS Boots OS) – a system call that allows Linux to boot another OS without leaving the 32-bit protected mode or using the BIOS
Overlaying the kernel (in kernel mode)
  read a file into memory not occupied by the running kernel
  move critical structures (page tables, boot arguments, root partition location, log buffer, etc) into a safe place
  turn off interrupts (point of no return – check all errors)
  switch memory to the new page tables
  copy the final bootstrap code (that copies the kernel to 0x100000 and jumps to it) to a safe place where it will not be overwritten by the new kernel
  jump to the final bootstrap code that will do its thing

## Slide 17: LOBOS Implementation
5 major pieces in about 300 lines
  entry for the new system call in arch/i386/kernel/entry.S
  some additions to arch/i386/kernel/head.S to make space for the critical kernel data that will be copied
    a few additional pages at the beginning of the kernel virtual address space, not used in normal kernel operation, hence safe
  the code to read in the new file in kernel/sys.c
    sys_lobos(char* file) looks up the file and calls read_exec()
  the code to switch off interrupts, move the critical data, and switch over to the new page tables, in arch/i386/kernel/process.c
    os_restart(), some assembly required…
  the code to copy the new kernel to the right place and jump to it, in kernel/sys.c
can be called from userspace, command line
faster than BIOS (a lot of waiting in BIOS is for DOS 1.0 support tasks(

## Slide 18: Related Work: bootimg, Two Kernel Monte (TKM)
bootimg
  allows a userspace program to read a file in and boot a new image via a system call
  turns VM (paging) off (but not i386-style segmentation)
  the user buffer (in VM) has to be copied into kernel memory accessible without VM
  relies on kernel components being in physically contiguous memory
  1100 LOC (600 architecture-dependent), some structures (GDT) need to be maintained in sync with kernel
  can be used with LinuxBIOS
  thorough permissions checking, ramdisk support
Two Kernel Monte (TKM)
  turns off both VM and i386 segmentation
  builds and internal virtual-to-physical page map (so it can still get to kernel)
  relies on BIOS to reset hardware (e.g. video card) after reboot
  cannot be used with LinuxBIOS (because of reliance on the BIOS)
Both require an external program to boot a new image (LOBOS doesn’t)

## Slide 19: Status
Mainboards, chipsets
  Too many to list, quite a few vendors, but not guaranteed that yours will work
  Many are marked as “unstable”
  Better chance with Intel than with others
Architectures
  Alpha, K8, K7, PowerPC, P4, PIII, PII, Cyrix (VIA), Geode (now AMD) and SC520 (AMD).
  PPC (some: Motorola Sandpoint is reported as working, IBM 970 port in progress)
OS
  Linux (but of course)
  OpenBSD
  Win2K (LILO and GRUB support with the help of BOCHS)
Deployment
  the biggest, baddest, fastest clusters built by LinuxNetworx for LANL
  Pentium and K8

## Slide 20: LinuxBIOS in Real Life (Have You Even Been to Los Alamos?)
Already there:
  The Superdense Server project (IBM Austin)
    http://www.research.ibm.com/journal/rd/475/felter.pdf
Potentially:
  iSCSI/iBOOT
  Experimental hardware projects
Difficulties:
  Convince everybody there is a commercial advantage
  Convince Marketing that they can convince potential customers…
  Convince Legal that open source (GPL) is not exactly AIDS
  Deal with existing and emerging de-facto standards (e.g. EFI)
Create a market:
  LANL RFPed 2 clusters requiring LinuxBIOS at $19MM – vendors lined up

## Slide 21: Summary
A promising direction in general – let’s get rid of the BIOS!
For prototype development:
  tinkering with hardware may cause pain in various parts of anatomy, or sudden death
  not clear if target hardware or prototype hardware is supported
    quite a bit of hacking may be required – not necessarily a bad thing
  open source - a major advantage for hacking
  limited OS support, though LILO/GRUB are reported to work, so there is hope
For product development:
  need a limited range of hardware to work
  tinkering with hardware is not a problem
  quite a few advantages in deployment
    fast boot
    flexible
    concurrent remote access, logging, etc
  biggest question – hardware and OS support

## Slide 22: Further Information
Main website:
  http://www.linuxbios.org
“Putting Linux on Your Motherboard” by Antony Stone, Linux Magazine, March 2003, p. 76.
  http://www.linuxbios.org/papers/linux-magazine/LinuxBIOS.pdf
“LinuxBIOS at Four” by Ron Minnich, Linux Journal, February 2004.
  http://www.linuxjournal.com/print.php?sid=7170
“LOBOS (Linux OS Boots Linux OS): Booting a Kernel in 32-bit Mode” by Ron Minnich, the 4th Annual Linux Showcase and Conference, October 2000
  http://www.linuxbios.org/papers/als00/lobos.pdf
Other papers:
  http://www.linuxbios.org/papers
Mailing list
  http://www.clustermatic.org/mailman/listinfo/linuxbios
BIOS history: “Accidental Empires” by Robert X. Cringely, HarperBusiness