## Slide 1: High Performance Computing with Linux clusters
Mark Silberstein
marks@tx.technion.ac.il
Technion 9.12.2002
Haifux Linux Club

## Slide 2: What to expect
You will learn...
  Basic terms of HPC and Parallel / Distributed systems
  What is A Cluster and where it is used
  Major challenges and some of their solutions in building / using / programming clusters
You will NOT learn…
  How to use software utilities to build clusters
  How to program / debug / profile clusters
  Technical details of system administration
  Commercial software cluster products
  How to build High Availability clusters
You can construct cluster yourself!!!!
Notes: 2 parts: theoretical (basics) & technical ( overview of different systems )

## Slide 3: Agenda
High performance computing
Introduction into Parallel World
Hardware
Planning , Installation & Management
Cluster glue – cluster middleware and tools
Conclusions

## Slide 4: HPC: characteristics
Requires TFLOPS, soon PFLOPS ( 250 )
  Just to feel it: P-IV XEON 2.4G – 540 MFLOPS
Huge memory (TBytes)
  Grand challenge applications ( CFD, Earth simulations, weather forecasts...)
Large data sets (PBytes)
  Experimental data analysis ( CERN - Nuclear research )
    Tens of TBytes daily
Long runs (days, months)
  Time ~ Precision ( usually NOT linear )
    CFD -> 2 X precision => 8 X time
Notes: Typical problem: partial differential equation solution. Solution: grid, iterations over dimensions and time.

## Slide 5: HPC: Supercomputers
Not general-purpose machines, MPP
State of the art ( from TOP500 list )
  NEC: EarthSimulator 35860 TFLOPS
    640X8 CPUs, 10 TB memory, 700 TB disk-space, 1.6 PB mass store
    Area of computer = 4 tennis courts, 3 floors
  HP: ASCI Q, 7727 TFLOPS (4096 CPUs)
  IBM: ASCI white, 7226 TFLOPS (8192 CPUs)
  Linux NetworX: 5694 TFLOPS, (2304 XEON P4 CPUs)
Prices:
  CRAY: $ 90.000.000

## Slide 6: Everyday HPC
Examples from everyday life
  Independent runs with different sets of parameters
    Monte Carlo
  Physical simulations
  Multimedia
    Rendering
    MPEG encoding
  You name it….
Do we really need Cray for this???

## Slide 7: Clusters: “Poor man's Cray”
PoPs, COW, CLUMPS NOW, Beowulf….
Different names, same simple idea
  Collection of interconnected whole computers
  Used as single unified computer resource
Motivation:
  HIGH performance for LOW price
    CFD Simulation runs 2 weeks (336 hours)on single PC. It runs 28 HOURS on cluster of 20 Pcs
    10000 Runs each one 1 minute. Total ~ 7 days. With cluster if 100 PCs ~ 1.6 hours

## Slide 8: Why clusters & Why now
Price/Performance
Availability
Incremental growth
Upgradeability
Potentially infinite scaling
Scavenging (Cycle stealing)
Advances in
  CPU capacity
  Advances in Network Technology
Tools availability
Standartisation
LINUX

## Slide 9: Why NOT clusters
Parallel system
Cluster
    Installation
    Administration &Maintenance
    Difficult programming model
?
Notes: Pictures are taken from “In search of Clusters”, G. Pfister

## Slide 10
Agenda
High performance computing
Introduction into Parallel World
Hardware
Planning , Installation & Management
Cluster glue – cluster middleware and tools
Conclusions

## Slide 11: “Serial man” questions
“I bought dual CPU system, but my MineSweeper does not work faster!!! Why?”
“Clusters..., ha-ha..., does not help! My two machines are connected together for years, but my Matlab simulation does not run faster if I turn on the second”
“Great! Such a pitty that I bought $1M SGI Onix!”

## Slide 12: How program runs on multiprocessor
P
P
P
P
P
P


Process
Processor
Thread
P
Operating
System
Shared Memory
MP
Application

## Slide 13: Cluster: Multi-Computer
P
P
OS
Physical Memory
OS
Physical Memory
Network
P
P
CPUs
CPUs
MIDDLEWARE
MIDDLEWARE

## Slide 14: Software Parallelism Exploiting computing resources
Data Parallelism
  Single Instructions, Multiple Data (SIMD)
    Data is distributed between multiple instances of the same process
Task parallelism
  Multiple Instructions, Multiple Data (MIMD)
Cluster terms
  Single Program, Multiple Data
  Serial Program, Parallel Systems
    Running multiple instances of the same program on multiple systems

## Slide 15: Single System Image (SSI)
Illusion of single computing resource, created over collection of computers
SSI level
  Application & Subsystems
  OS/kernel level
  Hardware
SSI boundaries
  When you are inside – cluster is a single resource
  When you are outside – cluster is a collection of PCs

## Slide 16: Parallelism & SSI
Levels of SSI
Kernel & OS
MOSIX
cJVM
PVFS
ClusterPID
PVM
Explicit parallel programming
MPI
Programming Environments
HPF
Split-C
OpenMP
Resource Management
Condor
PBS
Score DSM
ScaLAPAC
Ideal SSI
Clusters are
NOT there
Ideal SSI
Transparency
Parallelism Granularity
Process
Application
Job
Serial
application
Instruction

## Slide 17
Agenda
High performance computing
Introduction into Parallel World
Hardware
Planning , Installation & Management
Cluster glue – cluster middleware and tools
Conclusions

## Slide 18: Cluster hardware
Nodes
  Fast CPU, Large RAM, Fast HDD
    Commodity off-the-shelf PCs
    Dual CPU preferred (SMP)
Network interconnect
  Low latency
    Time to send zero sized packet
  High Throughput
    Size of network pipe
Most common case: 1000/100 Mb Ethernet

## Slide 19: Cluster interconnect problem
High latency ( ~ 0.1 mSec ) & High CPU utilization
  Reasons: multiple copies, interrupts, kernel-mode communication
Solutions
  Hardware
    Accelerator cards
  Software
    VIA (M-VIA for Linux – 23 uSec)
    Lightweight user-level protocols: ActiveMessages, FastMessages

## Slide 20: Cluster Interconnect Problem
Insufficient throughput
  Channel bonding
High performance network interfaces+ new PCI bus
  SCI, Myrinet, ServerNet
    Ultra low application-to-application latency (1.4uSec) - SCI
    Very high throughput ( 284-350 MB/sec ) – SCI
10 GB Ethernet & Infiniband

## Slide 21: Network Topologies
Switch
  Same distance between neighbors
  Bottleneck for large clusters
Mesh/Torus/Hypercube
  Application specific topology
  Difficult broadcast
Both

## Slide 22
Agenda
High performance computing
Introduction into Parallel World
Hardware
Planning , Installation & Management
Cluster glue – cluster middleware and tools
Conclusions

## Slide 23: Cluster planning
R
U
U
U
R
R
G
Cluster farm
Cluster environment
  Dedicated
    Cluster farm
      Gateway based
      Nodes Exposed
  Opportunistic
    Nodes are used as work stations
  Homogeneous
  Heterogeneous
    Different OS
    Different HW
U
User of resource
G
R
Resource
Gateway
U
R
U
R
U
R

## Slide 24: Cluster planning (Cont.)
Cluster workloads
  Why to discuss this? You should know what to expect
    Scaling: does adding new PC really help?
  Serial workload – running independent jobs
    Purpose: high throughput
    Cost for application developer: NO
    Scaling: linear
  Parallel workload – running distributed applications
    Purpose: high performance
    Cost for application developer: High in general
    Scaling: depends on the problem and usually not linear

## Slide 25: Cluster Installation Tools
Installation tools requirements
  Centralized management of initial configurations
  Easy and quick to add/remove cluster node
  Automation (Unattended install)
  Remote installation
Common approach (SystemImager,SIS)
  Server holds several generic image of cluster-node
  Automatic initial image deployment
    First boot from CD/floppy/NW invokes installation scripts
  Use of post-boot auto configuration (DHCP)
  Next boot – ready-to-use system

## Slide 26: Cluster Installation Challenges (cont.)
Initial image is usually large ( ~ 300MB)
  Slow deployment over network
  Synchronization between nodes
Solution
  Use Root on NFS for cluster nodes (HUJI – CLIP)
    Very fast deployment – 25 Nodes for 15 minutes
    All Cluster nodes backup on one disk
    Easy configuration update (even when a node is off-line)
    NFS server: Single point of failure
  Use of shared FS (NFS)

## Slide 27: Cluster system management and monitoring
Requirements
  Single management console
  Cluster-wide policy enforcement
    Cluster partitioning
  Common configuration
    Keep all nodes synchronized
  Clock synchronization
  Single login and user environment
  Cluster-wide event-log and problem notification
Automatic problem determination and self-healing

## Slide 28: Cluster system management tools
Regular system administration tools
  Handy services coming with LINUX:
    yp – configuration files, autofs – mount management, dhcp – network parameters, ssh/rsh – remote command execution, ntp - clock synchronization, NFS – shared file system
Cluster-wide tools
  C3 (OSCAR cluster toolkit)
    Cluster-wide …
      Command invocation
      Files management
    Nodes Registry

## Slide 29: Cluster system management tools
Cluster-wide policy enforcement
  Problem
    Nodes are sometimes down
    Long execution
  Solution
    Single policy - Distributed Execution (cfengine)
    Continious policy enforcement
      Run-time monitoring and correction

## Slide 30: Cluster system monitoring tools
Hawkeye
  Logs important events
  Triggers for problematic situations (disk space/CPU load/memory/daemons)
  Performs specified actions when critical situation occurs (Not implemented yet)
Ganglia
  Monitoring of vital system resources
  Multi-cluster environment

## Slide 31: All-in-one Cluster tool kits
SCE http://www.opensce.org
  Installation
  Monitoring
  Kernel modules for cluster wide process management
OSCAR http://oscar.sourceforge.net
ROCS http://www.rocksclusters.org
  Snapshot of available cluster installation/management/usage tools

## Slide 32
Agenda
High performance computing
Introduction into Parallel World
Hardware
Planning , Installation & Management
Cluster glue – cluster middleware and tools
Conclusions

## Slide 33: Cluster glue - middleware
Various levels of Single System Image
  Comprehensive solutions
    (Open)MOSIX
    ClusterVM ( java virtual machine for cluster )
    SCore (User Level OS)
    Linux SSI project (High availability)
  Components of SSI
    Cluster File system (PVFS,GFS, xFS, Distributed RAID)
    Cluster-wide PID (Beowulf)
    Single point of entry (Beowulf)

## Slide 34: Cluster middleware
Resource management
  Batch-queue systems
    Condor
    OpenPBS
Software libraries and environment
  Software DSM http://discolab.rutgers.edu/projects/dsm
  MPI, PVM, BSP
  Omni OpenMP
  Parallel debuggers and profiling
    PARADYN
    TotalVIEW ( NOT free )

## Slide 35: Cluster operating system Case Study – (open)MOSIX
Automatic load balancing
  Use sophisticated algorithms to estimate node load
Process migration
  Home node
  Migrating part
Memory ushering
  Avoid thrashing
Parallel I/O (MOPI)
  Bring application to the data
    All disk operations are local

## Slide 36: Cluster operating system Case Study – (open)MOSIX (cont.)
  Ease of use
  Transparency
  Suitable for multi-user environment
  Sophisticated scheduling
  Scalability
  Automatic parallelization of multi-process applications
  Generic load balancing not always appropriate
  Migration restrictions
    Intensive I/O
    Shared memory
  Problem with explicitly parallel/distributed applications (MPI/PVM/OpenMP)
  OS - homogeneous
  NO QUEUEING

## Slide 37: Batch queuing cluster system
Assumes opportunistic environment
  Resources may fail/station shutdown
Manages heterogeneous environment
  MS W2K/XP, Linux, Solaris, Alpha
Scalable (2K nodes running)
Powerful policy management
Flexibility
Modularity
Single configuration point
User/Job priorities
Perl API
DAG jobs
Goal: To steal unused cycles
  When resource is not in use and release when back to work

## Slide 38: Condor basics
Job is submitted with submission file
  Job requirements
  Job preferences
Uses ClassAds to match between resources and jobs
  Every resource publishes its capabilities
  Every job publishes its requirements
Starts single job on single resource
  Many virtual resources may be defined
Periodic check-pointing (requires lib linkage)
If resource fails – restarts from the last check-point

## Slide 39: Condor in Israel
Ben-Gurion university
  50 CPUs pilot installation
Technion
  Pilot installation in DS lab
  Possible modules developments for Condor high availability enhancements
  Hopefully further adoption

## Slide 40: Conclusions
Clusters are very cost efficient means of computing
You can speed up your work with little effort and no money
You should not necessarily be a CS professional to construct cluster
You can build cluster with FREE tools
With cluster you can use idle cycles of others

## Slide 41: Cluster info sources
Internet
  http://hpc.devchannel.org
  http://sourceforge.net
  http://www.clustercomputing.org
  http://www.linuxclustersinstitute.org
  http://www.cs.mu.oz.au/~raj (!!!!)
  http://dsonline.computer.org
  http://www.topclusters.org
Books
  Gregory F. Pfister, “In search of clusters”
  Raj. Buyya (ed), “High Performance Cluster Computing”

## Slide 42: The end